## Slide 1
Error Correction and Syndrome Calculation
Using MATLAB
Vishvendra Singh
Sameer Gautam
( 1DS18EC156 )
( 1DS18EC143 )
By
Objective:
(Linear Block Codes)
Dayananda Sagar College of Engineering
( Shavige Malleshwara Hills, Kumaraswamy Layout, Bengaluru – 560 078 )
Department of Electronics and Communication Engineering

## Slide 2
CONTENTS
Introduction
Block Diagram Employing Error Control Coding
Linear Block Codes
Matrix Description and Representation of Code vectors
Parity Check Matrix
Error Correction and Syndrome
Algorithm to find the Syndrome and correct the error
Example
Applications

## Slide 3
INTRODUCTION
The purpose of error control coding is to enable the receiver to detect or even correct the errors by introducing some redundancies in to the data to be transmitted.
There are basically two mechanisms for adding redundancy:
1.Block coding
2.Convolutional coding
Error is a condition when the output information does not match with the input information. During transmission, digital signals suffer from noise that can introduce errors in the binary bits travelling from one system to other. That means a 0 bit may change to 1 or a 1 bit may change to 0.
System 1
System 2

## Slide 4
Channel
Encoder
Modulator
Noisy
Communication
Channel
Demodulator
Channel
Decoder
n- bit Codeword
n – bit Codeword
(k-Message
bits)
(n-k) Check
bits)
Input Message
Output Message
BLOCK DIAGRAM OF DIGITAL COMUNICATION SYSTEM EMPLOYING ERROR CONTROL CODING

## Slide 5
LINEAR BLOCK CODES
The encoder generates a block of n coded bits from k information bits and we call this as (n, k) block codes. The coded bits are also called as code word symbols.
• Let C1 and C2 be any two code words(n-bits)belonging to a set of (n, k) block code
• If the convolution sum of C1 and C2 is also a n-bit code word belonging to the same set of (n,k) block code, then such a block code is called (n,k) linear block code.
Message, D
Codeword, C

## Slide 6
Let the message block of k-bits be represented as a “row-vector” called message vector given by [D]={ d1, d2, .....dk}
2k code-vectors can be represented by C={c1,c2,....cn}
Also, ci=di for all i=1,2,......k ie.
Matrix description of linear block code
(n-k check bits)
(k-Message bits digits)
[C]= {c1,c2,........,ck, ck+1, ck+2,.......cn}
For a linear code, there exists a kxn generator matrix G such that
[C]= [D].[G]

## Slide 7
Representation of Code Vector
1 | 0 | 0 | ……. | 0
0 | 1 | 0 | ……. | 0
0 | 0 | 1 | ……. | 0
. | . | . |  | 0
0 | 0 | 0 | ……. | 1
P11 | P12 | P13 | … | P1.(n-k)
P21 | P22 | P23 | … | P2.(n-k)
P31 | P32 | P33 | … | P3.(n-k)
. | . | . | . | .
Pk1 | Pk2 | Pk3 | . | Pk.(n-k)
(K x k)
(K x n)
c 1 | c 2 | c 3 | ….. | c n
d1 | d2 | d3 | ….. | dn
=
[C] = [D].[G]
where,
[G] = [Ik ¦ P] (k x n) where Ik is unit matrix of order ‘k’.
[P]= Parity matrix of order k x (n-k).
Also , Generator Matrix can be represented as [G] = [P ¦ Ik]

## Slide 8
PARITY CHECK MATRIX (H)
When G is systematic, it is easy to determine the parity check matrix H as:
H = [𝑃𝑇 𝐼(𝑛−𝑘) ]
1 | 0 | 0 | ……. | 0
0 | 1 | 0 | ……. | 0
0 | 0 | 1 | ……. | 0
. | . | . |  | 0
0 | 0 | 0 | ……. | 1
P11 | P21 | P31 | … | Pk1
P12 | P22 | P32 | … | Pk2
P13 | P23 | P33 | … | Pk3
. | . | . | . | .
P1.(n-k) | P2.(n-k) | P3.(n-k) | . | Pk.(n-k)
=
The H matrix is used in error correction and is of order (n-k) x (n).
The code words should satisfy (n-k) Parity check equation:
[D].[G].[HT] = 0
[C].[HT] = 0

## Slide 9
Error Correction and Syndrome
For a code word ‘c’, transmitted over a noisy channel, let ‘r’ be the received vector at the output of the channel with error ‘e’.
The error-vector or error pattern ‘e’ is defined as difference between ‘r’ and ‘c’ ie. e=r - c
1, if r ≠c 0, if r=c
i
e =
c
e
r = c + e

## Slide 10
Properties of Syndrome:
The syndrome depends only on the error pattern and not on the transmitted code word.
s = (c+e). HT = c. HT + e HT = e. HT
All the error pattern differing by atleast a code word have the same syndrome s.
The Error Syndrome of received vector ‘r’ is given by:
S = r.HT = (s1, s2, s3,.......,s(n-k))

## Slide 11
Algorithm to find the syndrome and correct the error
Enter the Parity Matrix P and the values of n and k.
Enter the received vector R.
Generate the Generator Matrix G and Parity Check Matrix H.
Generate the code vector CV using 2^k message vectors denoted by U.
Generate the transpose of Parity Check Matrix H and calculate the syndrome S using the given formula.
The error bit and the corrected codeword are stored and displayed.
Generator Matrix and Parity Check Matrix
Outputs
Code Vectors using the Message Vectors
Calculation of Syndrome S
Correction of Error Bit
Inputs
(Using MATLAB Code)

## Slide 12
Example: For a Systematic (6,3) linear block code, Parity Matrix is given,
1. Display all Possible Code vectors.
2. If the Received Vector [R]=[110011], Find and display
the Syndrome, Detect and Correct the error.
1 | 1 | 1
1 | 1 | 0
1 | 0 | 1
[P] =
(3x3)
INPUTS: [P], n=6, k=3, [R]=[110011]
1 | 1 | 1
1 | 1 | 0
1 | 0 | 1
[G] =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
[C]=[D].[G]
Where, [D]=[d1 d2 d3 ]
[C]=[d1 d2 d3 (d1+d2+d3) (d1+d2) (d1+d3)]
By using message signals [d1 d2 d3 ], calculating Code vectors:

## Slide 13
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0
C =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
[H] =
1 | 1 | 1
1 | 1 | 0
1 | 0 | 1
1.
2.
[S] = [R].[HT]
= [110011].
1 | 1 | 1
1 | 1 | 0
1 | 0 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
[S]= [ 0 1 0 ]
The Syndrome Vector [S] is present in the 5th row of HT, So, the 5th bit from left in [R] has an error.
1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1
Received Vector
Corrected Vector
Error

## Slide 14
Thank you!